U.S. GEOLOGICAL SURVEY
                WATER-RESOURCES INVESTIGATIONS REPORT 93-4076

                         HYDRO-CLIMATIC DATA NETWORK
                                    (HCDN)
                        STREAMFLOW DATA SET, 1874-1988

                  [This is the \DOCFILES\DATAINFO.DOC file]


                              THE HCDN DATABASE

         The HCDN data base contains both the streamflow data and
      information identifying and describing each station in the HCDN.
      The following fields constitute the identifying and descriptive
      information.  Each field is available within the GSSEARCH search
      program to select stations for retrieval.  Most fields are
      available within the HCDR search program (although sometimes with
      different names) to select stations for retrieval.  In addition,
      all the fields are available in plain text (ASCII) tables in the
      \HCDN directory which can be searched by other mechanisms (e.g.,
      word processor) the user has available.


      Sta_Num     Station number - the 8 digit station number uniquely
                     identifying the streamflow station.
      Sta_Name    Station name - the 48 character name of the station.
      HUC         The 8 digit Hydrologic Unit Code identifying the
                     drainage basin.  The first two digits of the HUC
                     specify the Water Resources Council region.  The
                     second two digits specify the sub-basin.  The next
                     two digits give the accounting unit.  The final two
                     digits give the cataloging unit.
      Region      The name of the hydrologic region in which the station
                     lies.
      Sub_Region  The name of the sub-region in which the station lies.
      Drain_Area  The area of the drainage basin in square miles.
      P_Non_Cntb  The percentage of the drainage area which is
                     non-contributing.
      Num_Years   Number of complete water years of record for this
                     station.
      Time_Scale  A one character code which indicates the shortest time
                     scale at which the data is suitable for use in
                     climatic analysis.
                        D - Values at any time scale are suitable.
                               Daily, monthly, and annual values are
                               provided.
                        M - Only monthly or longer term values are
                               suitable; however, daily, monthly, and
                               annual values are provided.
                        N - No data is suitable and no data is provided.
      Portion     A one character code which indicates whether the
                     entire gaged record, or only a subset of it, is
                     suitable for use in climatic analysis.  No record
                     after WY1988 has been examined for inclusion in the
                     HCDN.
                        E - The entire period of record, but not after
                               WY1988, is suitable and provided.
                        P - Only part of the gaged record is suitable
                               and provided.
                        N - No data is suitable and no data is provided.
      N_Comments  Number of lines of comments for this station.
      Comments    Comments addressing the suitability of the streamflow
                     at this station for climatic analysis.
      District    The two character abbreviation of the USGS Water
                     Resources Division District which services the
                     gaging station.
      State       The two character abbreviation of the state in which
                     the gaging station is located.
      County      The code number of the county in which the gaging
                     station is located.  See Federal Information
                     Processing Standards Publication (FIPS PUBS) 6-3
                     for a list of these codes.
      Latitude    Latitude of the gaging station in the form DDMMSS
                     where D is degrees, M is minutes, and S is seconds.
      Lat_Hem     Hemisphere of the latitude - N for Northern and S for
                     Southern.
      Longitude   Longitude of the gaging station in the form DDDMMSS.
      Long_Hem    Hemisphere of the longitude - W for Western and E for
                     Eastern.
      Datum       Datum - an arbitrary reference point generally
                     corresponding to the elevation of the gaging
                     station in feet above the National Geodetic
                     Vertical Datum of 1929.  A value of -99.00
                     indicates a missing value.
      Benchmark   Benchmark indicator - B if the station is a Benchmark
                     station, blank otherwise.
      NWC         Current Conditions indicator - C if the station is a
                     Current Conditions station, blank otherwise.
      Slope       Main channel slope, in feet per mile, measured at
                     points 10- and 85-percent of stream length upstream
                     from gage.
      Length      Stream length, in miles, measured along the channel
                     from gage to basin divide.
      Elevation   Mean basin elevation, in feet above mean sea level,
                     measured from topographic maps by transparent grid
                     sampling method (20 to 80 points in basin were
                     sampled).
      P_Storage   Percent storage - Area of lakes, ponds, and swamps in
                     percent of contributing drainage area, measured by
                     the grid sampling method.
      P_Lake      Percent lake area - Area of lakes and ponds, in
                     percent of contributing drainage area, measured by
                     the grid sampling method.
      P_Forest    Percent forest - Forested area, in percent of
                     contributing drainage area, measured by the grid
                     sampling method.  The resolution and scale of the
                     underlying maps varied widely.
      P_Glacier   Percent glacier - Area of glaciers, in percent of
                     contributing drainage area.
      Soil_Index  Soil index, in inches, a relative measure of potential
                     infiltration (soil water storage), from Soil
                     Conservation Service.  The soil index was
                     determined from maps that were necessarily highly
                     generalized and may be relatively coarse in
                     resolution when applied to small drainage areas.
      Precip      Mean annual precipitation, in inches, from U.S.
                     Weather Bureau series, "Climates of States", 1959-
                     61: grid sampling methods used if isohyetal map is
                     available, otherwise anomaly map constructed (WSP
                     1580-D, 1964).
      Precip_Int  Precipitation intensity; 24-hour rainfall, in inches,
                     expected on the average of one each 2 years.
                     (Estimated from U.S. Weather Bureau Technical Paper
                     40 (1961) except for western States where NOAA
                     Atlas 2 exists).
      Jan_Min_T   Mean minimum January temperature, in degrees F, from
                     U.S. Weather Bureau series, "Climates of States",
                     1959-61.
      Year_Table  Indicator for whether there is data for a particular
                     water year.  The presence of a year indicates that
                     the entire water year is included in the HCDN.